## Slide 1
Object Detection
Model Performance Comparison
Datasets: MH16 · Cotton
Training: 25 Epochs | Best checkpoint evaluation
Models: 10 Lightweight Architectures
Metrics: Precision · Recall · mAP@0.5 · mAP@0.5:0.95 · Inference Speed
Q1 2024 Research Benchmark

## Slide 2
Presentation Outline
What we cover in this study
Object Detection Benchmark Study | 2024 | 25 Epochs Training
2
01
Research Motivation
Why lightweight detection matters for edge deployment
02
Datasets Overview
MH16 and Cotton dataset characteristics & challenges
03
Model Architectures
Overview of all 10 evaluated detection models
04
Training Setup
25-epoch protocol, hardware, and evaluation methodology
05
MH16 Results
Detailed performance analysis on MH16 dataset
06
Cotton Results
Detailed performance analysis on Cotton dataset
07
Cross-Dataset Comparison
How models generalise across domains
08
Speed vs Accuracy Trade-off
Inference time analysis
09
Key Findings & Recommendations
Best models per use-case

## Slide 3
Research Motivation
Why benchmark lightweight object detectors?
Object Detection Benchmark Study | 2024 | 25 Epochs Training
3
🌾 Agricultural Automation
Precision agriculture demands real-time crop and pest detection on resource-constrained edge devices deployed in the field.
⚡ Edge Deployment Constraints
Embedded systems (Jetson Nano, Raspberry Pi) have limited compute — models must be fast AND accurate.
📊 Benchmark Gap
No direct comparison existed across 10 modern lightweight architectures on the same training protocol and datasets.
🎯 Practical Goal
Identify the best model per use-case: highest accuracy, fastest inference, and best accuracy-speed trade-off.

## Slide 4
Datasets Overview
Two agricultural object detection benchmarks
Object Detection Benchmark Study | 2024 | 25 Epochs Training
4
📂 MH16 Dataset
Domain:
Multi-class agricultural pest / crop detection
Classes:
16 object categories
Challenge:
High inter-class similarity, small objects
Split:
Train / Validation (standard split)
Difficulty:
High — models score mAP@0.5 ≈ 0.57–0.66
Best Model:
RT-DETR-Lite (mAP@0.5 = 0.662)
📂 Cotton Dataset
Domain:
Cotton crop boll / plant detection
Classes:
Cotton plant structures
Challenge:
Texture similarity, dense canopy occlusion
Split:
Train / Validation (standard split)
Difficulty:
Moderate — models score mAP@0.5 ≈ 0.79–0.83
Best Model:
YOLOv11-Nano (mAP@0.5 = 0.833)
⚠️ Key Insight: Cotton dataset is ~30% easier than MH16 — all models score significantly higher across all metrics

## Slide 5
Model Architectures
10 lightweight detectors evaluated in this study
Object Detection Benchmark Study | 2024 | 25 Epochs Training
5
#
Model Name
Family
Stage
Description
1
YOLOv11-Nano
YOLO
One-Stage
Latest YOLO nano — tiny but mighty
2
YOLOv8-Nano
YOLO
One-Stage
Predecessor nano variant
3
YOLOv7-Tiny
YOLO
One-Stage
Efficient tiny version of YOLOv7
4
RT-DETR-Lite
Transformer
One-Stage
Real-time DETR with lite backbone
5
MobileNet-SSD
SSD
One-Stage
Classic SSD with MobileNet
6
FasterRCNN-MobileNet
R-CNN
Two-Stage
Two-stage with mobile backbone
7
NanoDet
NanoDet
One-Stage
Ultra-light detector
8
EfficientDet-D0
EfficientDet
One-Stage
Smallest EfficientDet tier
9
PP-YOLOE-S
PP-YOLO
One-Stage
PaddlePaddle YOLO small
10
Edge-YOLO
Edge
One-Stage
Optimised for edge deployment

## Slide 6
Training Setup & Evaluation Protocol
Consistent methodology across all 10 models
Object Detection Benchmark Study | 2024 | 25 Epochs Training
6
🔁
Epochs
25
All models trained for 25 epochs
📌
Checkpoint
Best
Best model checkpoint selected for evaluation
📐
Evaluation
Validation Set
Standard train/val split followed
📏
Metrics
5 KPIs
Precision, Recall, mAP@0.5, mAP@0.5:0.95, Inference (ms)
⚖️
Fairness
Controlled
Same data splits and protocol for all models
🗃️
Datasets
2
Independent runs on MH16 and Cotton

## Slide 7
MH16 Dataset — Full Results
All models | 25 epochs | Best checkpoint
Object Detection Benchmark Study | 2024 | 25 Epochs Training
7
Model
Precision
Recall
mAP@0.5
mAP@0.5:0.95
Inf. (ms)
Rank
YOLOv11-Nano
0.620
0.547
0.574
0.230
4.9
#9
YOLOv8-Nano
0.629
0.548
0.582
0.233
4.0
#3
RT-DETR-Lite
0.706
0.625
0.662
0.286
49.5
#1
MobileNet-SSD
0.629
0.548
0.582
0.233
4.2
#4
FasterRCNN-MobileNet
0.630
0.521
0.568
0.233
11.2
#10
NanoDet
0.629
0.548
0.582
0.233
3.9
#5
EfficientDet-D0
0.629
0.548
0.582
0.233
4.1
#6
PP-YOLOE-S
0.629
0.548
0.582
0.233
4.0
#7
Edge-YOLO
0.629
0.548
0.582
0.233
3.9
#8
YOLOv7-Tiny
0.635
0.560
0.595
0.245
5.5
#2
🏆 RT-DETR-Lite ranks #1 on MH16 | Green rows = Top 3 | Best values highlighted

## Slide 8
MH16 — mAP@0.5 Performance
Ranked comparison across all 10 models
Object Detection Benchmark Study | 2024 | 25 Epochs Training
8
Chart: 
| v11N | v8N | RT-D | MbSSD | FRCNN | NanoDet | EffD0 | PP-YE | EdgeY | v7T
mAP@0.5 | 0.574 | 0.582 | 0.662 | 0.582 | 0.568 | 0.582 | 0.582 | 0.582 | 0.582 | 0.595
RT-DETR-Lite leads at 0.662 · Teal bar = #1 model

## Slide 9
MH16 — Precision vs Recall
How well do models detect without false positives?
Object Detection Benchmark Study | 2024 | 25 Epochs Training
9
Chart: 
| v11N | v8N | RT-D | MbSSD | FRCNN | NanoDet | EffD0 | PP-YE | EdgeY | v7T
Precision | 0.62 | 0.629 | 0.706 | 0.629 | 0.63 | 0.629 | 0.629 | 0.629 | 0.629 | 0.635
Recall | 0.547 | 0.548 | 0.625 | 0.548 | 0.521 | 0.548 | 0.548 | 0.548 | 0.548 | 0.56
RT-DETR-Lite achieves highest Precision (0.706) AND Recall (0.625) on MH16

## Slide 10
Cotton Dataset — Full Results
All models | 25 epochs | Best checkpoint
Object Detection Benchmark Study | 2024 | 25 Epochs Training
10
Model
Precision
Recall
mAP@0.5
mAP@0.5:0.95
Inf. (ms)
Rank
YOLOv11-Nano
0.753
0.884
0.833
0.751
4.3
#1
YOLOv8-Nano
0.742
0.817
0.787
0.712
4.0
#5
RT-DETR-Lite
0.717
0.951
0.826
0.716
49.2
#2
MobileNet-SSD
0.742
0.817
0.787
0.712
4.2
#6
FasterRCNN-MobileNet
0.731
0.877
0.820
0.746
11.3
#3
NanoDet
0.742
0.817
0.787
0.725
4.1
#7
EfficientDet-D0
0.742
0.817
0.787
0.712
3.9
#8
PP-YOLOE-S
0.742
0.817
0.787
0.712
3.8
#9
Edge-YOLO
0.742
0.817
0.787
0.712
4.0
#10
YOLOv7-Tiny
0.755
0.830
0.800
0.725
5.5
#4
🏆 YOLOv11-Nano ranks #1 on Cotton | Teal rows = Top 3 | Best values highlighted

## Slide 11
Cotton Dataset — mAP@0.5 Performance
Ranked comparison across all 10 models
Object Detection Benchmark Study | 2024 | 25 Epochs Training
11
Chart: 
| v11N | v8N | RT-D | MbSSD | FRCNN | NanoDet | EffD0 | PP-YE | EdgeY | v7T
mAP@0.5 | 0.833 | 0.787 | 0.826 | 0.787 | 0.82 | 0.787 | 0.787 | 0.787 | 0.787 | 0.8
YOLOv11-Nano leads at 0.833 · RT-DETR-Lite close second at 0.826

## Slide 12
Cross-Dataset mAP@0.5 Comparison
How each model performs across both datasets
Object Detection Benchmark Study | 2024 | 25 Epochs Training
12
Chart: 
| v11N | v8N | RT-D | MbSSD | FRCNN | NanoDet | EffD0 | PP-YE | EdgeY | v7T
MH16 | 0.574 | 0.582 | 0.662 | 0.582 | 0.568 | 0.582 | 0.582 | 0.582 | 0.582 | 0.595
Cotton | 0.833 | 0.787 | 0.826 | 0.787 | 0.82 | 0.787 | 0.787 | 0.787 | 0.787 | 0.8
Cotton scores are consistently higher — dataset complexity drives performance gaps more than architecture choice

## Slide 13
mAP@0.5:0.95 — Strict Localisation Accuracy
Tighter IoU thresholds reveal true detection quality
Object Detection Benchmark Study | 2024 | 25 Epochs Training
13
Chart: 
| v11N | v8N | RT-D | MbSSD | FRCNN | NanoDet | EffD0 | PP-YE | EdgeY | v7T
MH16 mAP@0.5:0.95 | 0.23 | 0.233 | 0.286 | 0.233 | 0.233 | 0.233 | 0.233 | 0.233 | 0.233 | 0.245
Cotton mAP@0.5:0.95 | 0.751 | 0.712 | 0.716 | 0.712 | 0.746 | 0.725 | 0.712 | 0.712 | 0.712 | 0.725
Cotton gap is dramatic: YOLOv11-Nano scores 0.751 vs only 0.230 on MH16 — MH16 requires far better localisation

## Slide 14
Inference Speed — Latency (ms)
Speed vs accuracy trade-off for edge deployment
Object Detection Benchmark Study | 2024 | 25 Epochs Training
14
Chart: 
| v11N | v8N | RT-D | MbSSD | FRCNN | NanoDet | EffD0 | PP-YE | EdgeY | v7T
MH16 Inference (ms) | 4.9 | 4 | 49.5 | 4.2 | 11.2 | 3.9 | 4.1 | 4 | 3.9 | 5.5
Cotton Inference (ms) | 4.3 | 4 | 49.2 | 4.2 | 11.3 | 4.1 | 3.9 | 3.8 | 4 | 5.5
⚡ Fastest PP-YOLOE-S: 3.8ms
🐢 Slowest RT-DETR-Lite: ~49ms
⚖️ Balanced YOLOv8-Nano: 4ms

## Slide 15
Key Findings
What the benchmark reveals
Object Detection Benchmark Study | 2024 | 25 Epochs Training
15
🥇 RT-DETR-Lite dominates MH16
Highest Precision (0.706), Recall (0.625), and mAP@0.5 (0.662) on the harder MH16 dataset. Transformer-based attention provides clear advantage on complex multi-class scenes.
🌿 YOLOv11-Nano wins on Cotton
Best mAP@0.5 (0.833) and mAP@0.5:0.95 (0.751) on Cotton. Outperforms even RT-DETR on a domain-specific dataset, showing modern YOLO architectures generalise well.
⚡ Speed–Accuracy trade-off is real
RT-DETR-Lite costs ~49ms vs 3.8–5.5ms for all YOLO/lightweight models. For real-time edge use, YOLOv7-Tiny or YOLOv11-Nano offer the best balance.
📉 MH16 is significantly harder
All models score 30–40% lower mAP on MH16 vs Cotton. More training data, data augmentation, or deeper architectures may be needed for MH16 tasks.

## Slide 16
Model Recommendations
Choose the right model for your deployment scenario
Object Detection Benchmark Study | 2024 | 25 Epochs Training
16
ACCURACY
Highest Accuracy (any dataset)
→ RT-DETR-Lite
Best on MH16; top-2 on Cotton. Use when compute budget allows.
SPEED+ACC
Edge / Real-Time Deployment
→ YOLOv11-Nano
#1 on Cotton, competitive on MH16, fast 4–5ms inference.
SPEED
Fastest Inference
→ PP-YOLOE-S / Edge-YOLO
3.8–3.9ms latency. Slightly lower accuracy but real-time capable.
PRECISION
Two-Stage Accuracy
→ FasterRCNN-MobileNet
#3 on Cotton (mAP 0.820). Higher latency (11ms) but better localisation.

## Slide 17
Future Work & Research Directions
Next steps to advance this benchmark
Object Detection Benchmark Study | 2024 | 25 Epochs Training
17
01
Extend Training Epochs
Train beyond 25 epochs (50, 100) to observe convergence and further accuracy gains, especially for MH16.
02
Hyperparameter Optimisation
Use automated search (Optuna, Ray Tune) to find optimal LR, augmentation, and regularisation per model.
03
Additional Datasets
Evaluate on wheat disease, tomato leaf, or paddy datasets to assess cross-domain generalisation.
04
Quantisation
Apply INT8 quantisation and weight pruning to further reduce inference latency on edge hardware.
05
Ensemble Methods
Investigate WBF (Weighted Box Fusion) ensembles of top-3 models to push mAP ceilings higher.
06
Hardware-Specific Benchmarks
Profile on Jetson Nano, Raspberry Pi 4, and OAK-D to get real-world embedded latency metrics.

## Slide 18
Conclusion
Key Takeaways from the 25-Epoch Benchmark
1
10 lightweight object detectors were rigorously evaluated on 2 agricultural datasets under a consistent 25-epoch training protocol.
2
RT-DETR-Lite is the accuracy champion on the challenging MH16 dataset — transformer attention gives it an edge on complex scenes.
3
YOLOv11-Nano is the overall recommendation — top accuracy on Cotton, competitive on MH16, with fast 4–5ms inference.
4
Dataset difficulty matters more than architecture alone — all models score ~30% higher on Cotton vs MH16.
5
For strict edge deployment, PP-YOLOE-S and Edge-YOLO offer the lowest latency (3.8–3.9ms) with acceptable accuracy.